## Slide 1: Data Archiving
Kimberley 2017; Pilbara 2020; And so on

## Slide 2: 2 Options
 | Simply archive all the previously processed data “as is” | Develop a suite of tools that can automate processing of a field trip from a metadata database (a recipe basically)
Pros | Capitalise on work already done Potentially the fastest | Greatest consistency Full record of what was done to the data and in what order Can have multiple process levels, all handled consistently and transparently Will pull together all the tools that we have into one place Effort is recoverable and recipe can be updated anytime If we change our mind about something, we update the “recipe” and rerun. If we update a file or a method, we can rerun a whole experiment easily Will get everything into one language
Cons | Effort not recoverable Don’t end up with a suite of tools to use for future trips Work done is split between Matlab and Python, so there would be a bit of duplication of efforts in the archiving stage This is already done to some extent with the AGU “FAIR” requirement | Will require more effort in total More difficult to see the progress until the end (i.e. until the recipe is complete)

## Slide 3: Workflow
Metadata Database
Contains all deployment info but also maybe some info about corrections (e.g. clock offset) to automate re-processing
Process Level 1
[Quality Controlled Data]
Real units and base QC
Process Level 2
[Derived Products]
Stacked moorings
100% automated to get to this point
Process Level 3
[Interpreted products]
Process Level 4
[Knowledge Products]
Merged ADCPs
Filtered or smoothed data?
Replaced data?
Turbulence Calcs
Modal Amplitude
‘Background’ quantities
???
Mixing Efficiency ==0.2?
Fundamental idea of Option 2:
Can change anything and the processing can be automatically rerun for a whole expt. [keeping old versions]
Researchers can deviate from the path at any point, make their own changes, and these may or may not become the new-normal

## Slide 4: The Recipe
Database
  Simple CSV or PostgreSQL
Generic utilities
  E.g. Complete suite of automated QC conventions (IMOS); CF compliance checker; “Mooring stacker”; Timeseries analysis; Despiking
Base class which handles all interactions with a dataset
  E.g. Assigning QC codes with comments; Returning QC variables; Adding Comments; Tracking change history; Track processing applied; Ensuring CF compliance; Applying offsets
Super class per instrument which handles specifics
  E.g. Link to reader files (multiple allowed - crucial); Actually format the dataset; Quick plotting tools; Apply a standard suite of QC codes
Instrument specific utilities
  Rotations, transforms, bin mapping

## Slide 5: Coded and tested so far:
The base class
Instrument specific classes for all moored instrs.
Multiple readers [e.g. for handling corrupt files] all plug into the one system
Automation of CSV database to “Process Level 1” for all instruments above
CSV database to PostgreSQL database – should we wish to take that route in the future
All IMOS QC routines
Cf Compliance Checker
All of the higher process level tools [e.g. turbulence calcs, modal fitting] are coded in Python also – they just need to be plugged in
Output so far:
Kimberley 2017 profiler data to “Process Level 0”
Kimberley 2017 mooring data to “Process Level 1”
Kimberley 2017 mooring stack
Pilbara 2019 mooring data to “Process Level 1”

## Slide 6: Incremental that have led to full reprocess
z_nom, lat_nom and lon_nom all now dimension s of the files, not just attributes.
Improved handling of multipart files

## Slide 7: Process Levels – KISSME 2017
PL | Seabird 37, 39, 56 | Teledyne RDI | Signature | Vectors | Wetlabs | LISST | Profiling CTD | Profiling VMP | Profiling LISST
0 | * | * | * | * | * | Read Build structure Export Need to add attributes from the log file | Read Build structure Add attributes Export | Read Deconvolve Physical Units Build structure Add attributes Export | **
1 | Read Build structure Add attributes Calibrate InOutWaterQC Export | Read Build structure Add attributes InOutWaterQC TiltVelocitySimpleQC EchoIntensitySimpleQC ErrorVelocitySetQC CorrMagVelocitySetQC PercentGoodVelocitySetRDIQC Export NEED TO IMPLEMENT THE STANDARD FISH DETECTION | Read Build structure Add attributes InOutWaterQC TiltVelocitySimpleQC EchoIntensitySimpleQC CorrMagVelocitySetQC Export NEED TO IMPLEMENT THE ALONG-BEAM FISH DETECTION. | Read Build structure Add attributes InOutWaterQC FishDetectionQC CorrMagVelocitySetQC export The 6019 tilt sensor was broken. Tilt data is QCd out manually and commented | Read Build structure Add attributes _calibrate_device InOutWaterQC export | Need to implement CF compliance, associate qc_flags and add some auto qc_routines. | Need to implement CF compliance, associate qc_flags and add some auto qc_routines. | Need to implement CF compliance, associate qc_flags and add some auto qc_routines. | 
2 | Goring Nikora? Time filter/align Stack Moorings | ENU with BinMap Time filter/align Replace missing data Stack moorings | ENU Phase unwrap Replace missing data SIGNATURE BIN MAP NOT IMPLEMENTED | Replace missing Phase unwrap Goring Nikora? | Burst Median? Goring Nikora? |  | Transect | Replace missing Goring Nikora? | 
3 | Background quantities Modal fitting | Modal/harmonic fitting Velocity shear calcs Scotti et al. 2005? | Turbulence calcs Velocity shear calcs Scotti et al. 2005 | Turbulence Calcs Frame interference? This is a bit of a bespoke step, calculated after turbulence calcs. Not sure where this should come in? |  |  |  | Turbulence Calcs | 
* For these instruments I’m going straight to Process Level 1 [to save space on SSD]
** Not done at yet
Black=done; Blue=code tested but not in workflow; Orange = code needs further testing; Red=Known Issues

## Slide 8: Notebook structure
COMPLETE THIS.

## Slide 9: Archive Folder Structure and naming convention
COMPLETE THIS.

## Slide 10: Related Repos
iosonobert/pyODAS
iosonobert/turbotools
iosonobert/dallsporpoise
lkilcher/dolfyn
mrayson/mycurrents